## Slide 1: GHS/WHMIS 2015
(GHS - Globally Harmonized System)

## Slide 2: Introduction
WHMIS is aligning with the Globally Harmonized System (GHS) for classifying and labelling chemicals.
GHS does not replace WHMIS, but changes it.
Original WHMIS will be referred to as WHMIS 1988.
WHMIS aligned with GHS is called WHMIS 2015.
As WHMIS aligns with GHS, you will start to see new pictograms (symbols) and new requirements for labels and safety data sheets.

## Slide 3: WHMIS 2015
Introduces new:
Hazard classification criteria and classes
Standardized label requirements
Format for safety data sheets (SDS)

## Slide 4: Legislation
In February 2015, Canada amended the Hazardous Products Act and published the Hazardous Products Regulations in order to incorporate GHS into WHMIS.
Implementation of WHMIS 2015 will be completed over a 3 year transition period. During this transitional period, both WHMIS 1988 and 2015 can be used in the workplace.

## Slide 5: Legislation
WHMIS consists of three legislated components:
Labels
Safety Data Sheets (SDS)
Training

## Slide 6: WHMIS 1988 vs. WHMIS 2015
* The key responsibilities of suppliers, employers and workers remain the same under WHMIS 2015.
WHMIS 1988 | WHMIS 2015
Controlled Products Regulations | Hazardous Products Regulations
Controlled products | Hazardous products
6 hazard classes, 3 divisions | 30+ hazard classes, multiple categories
Label: Hatched border No standardized phrases | Label: Solid border Standardized phrases
Symbol in a black circle | Pictograms: symbol in a red square on its point (diamond)
Material Safety Data Sheets (MSDS) Must be updated every 3 years 9 sections | Safety Data Sheets (SDS) Must be updated when new information is available 16 sections

## Slide 7: Exclusions
Under WHMIS 2015, the following types of products continue to be excluded from labelling and SDS requirements:
Consumer products
Explosives
Pesticides
These products are excluded from WHMIS because they are regulated by different legislation. They may still be hazardous.

## Slide 8: WHMIS 2015 Pictograms

## Slide 9: Pictograms
Most hazard classes and categories will be assigned a symbol that indicates the type or severity of the hazard. Some less hazardous products may not have a pictogram.
WHMIS 2015 symbols are inside a red square set on its point (diamond shape).
The exception is the biohazard symbol that is inside a black circle. GHS does not have a biohazard pictogram so the pictogram was carried over from WHMIS 1988.

## Slide 10: New Pictograms
You should recognize many of the pictograms from your previous WHMIS 1988 training.
There are three new pictograms:
You may also see this environmental hazard pictogram:
However, it has not been adopted as part of WHMIS
2015 in Canada.

## Slide 11: Labels
WHMIS labels alert workers to the hazards of the product and provide any precautions to take when using the product.
Any product that belongs to a hazard class must have a label and a safety data sheet (SDS).
There are two kinds of labels: Supplier and Workplace Labels.

## Slide 12: Supplier Labels: Overview
A WHMIS 2015 label must contain the following information:
Product Identifier (name of product exactly as it appears on the container and safety data sheet)
Hazard Pictogram(s)
Signal Word
Hazard Statements
Precautionary Statements
Supplier Identification
The pictogram, signal word and hazard statements must be grouped together. The label must be in English and French.
WHMIS 2015 labels are no longer framed by a hatched border.

## Slide 13: Supplier Labels: Signal Words
Most, but not all, labels will have a signal word that expresses the severity of the hazard.
There are two signal words: DANGER and WARNING
DANGER is used for high level hazards.
WARNING is used for medium level hazards.
Only ONE signal word is required.
Lower hazard categories may not have a signal word on the label.

## Slide 14: Supplier Labels: Hazard Statements
WHMIS assigns standardized hazard statements. These statements describe the hazards of a product.
The words used in the hazard statements help to identify the degree of the hazard.
For example: fatal vs. harmful, will vs. may.

## Slide 15: Supplier Labels: Precautionary Statements
Standardized precautionary statements provide general precautions related to:
Storage
Use
First Aid
Personal protective equipment.
Emergency measures that should be followed in order to reduce or prevent harmful effects from the product.
*Always check the safety data sheet (SDS) for detailed precautions.

## Slide 16: Supplier Labels: Example
Product Identifier
Hazard Pictogram
Signal Word
Hazard Statements
Precautionary Statements
Supplier Information

## Slide 17: Workplace Labels
A workplace label is required when a hazardous product is poured into a new container.
This label must include:
Product Identifier/Name
Safe handling precautions, including optional pictograms
Reference to the safety data sheet (SDS)
Workplace labels can be printed from www.msdsforschools.ca.
There are two situations when a workplace label is not necessary. When a hazardous product is:
poured into a container and it is going to be used immediately, or
"under the control of the person who decanted it". If the person who poured the product into another container will be the only person using it, and the product will be used during one shift, a full workplace label is not required. HOWEVER, THE CONTAINER MUST STILL BE IDENTIFIED WITH THE PRODUCT IDENTIFIER (NAME).

## Slide 18: Workplace Label: Example 1
PRODUCT XYZ
Fatal if swallowed.
Causes skin irritation.
See SDS for more information.

## Slide 19: Workplace Label: Example 2
PRODUCT ABC
Fatal if swallowed.
Causes skin irritation.
Wear protective gloves.
See SDS for more information.

## Slide 20: WHMIS Hazard Groups
WHMIS 2015 uses two of the three GHS hazard groups: PHYSICAL and HEALTH. Canada has not adopted the Environmental hazard group.
Each group is broken down into multiple classes.
PHYSICAL
HAZARD GROUP
HEALTH HAZARD GROUP
PHYSICAL HAZARD GROUP CLASSES
HEALTH HAZARD GROUP CLASSES
WHMIS 2015

## Slide 21: WHMIS Hazard Groups: Categories & Subcategories
Each hazard group class is divided into categories.
Each category can be further divided in a subcategory.
PHYSICAL
HAZARD GROUP
HEALTH HAZARD GROUP
PHYSICAL HAZARD GROUP CLASSES
HEALTH HAZARD GROUP CLASSES
CATEGORIES
CATEGORIES
WHMIS 2015
SUBCATEGORIES
SUBCATEGORIES

## Slide 22: Categories & Subcategories
All hazard classes have at least one hazard category.
The category identifies the level of the hazard.
Categories are assigned a number (e.g. 1, 2, 3, 4). The lower the category number the more hazardous the hazard (i.e. 1 > 2 > 3 > 4).
Categories can also be referred to as types. Types are assigned a letter (e.g. A, B, C).
  Categories can be subdivided into subcategories (e.g. 1A, 1B, 1C).
The subcategory with the higher letter grade is more hazardous (i.e. 1A>1B>1C).
HIGH HAZARD
LOW HAZARD
Category 1
Category 2
Category 3
1A
1B
1C

## Slide 23: Physical Hazard Group
PHYSICAL
HAZARD GROUP
HEALTH HAZARD GROUP
PHYSICAL HAZARD GROUP CLASSES
HEALTH HAZARD GROUP CLASSES
CATEGORIES
CATEGORIES
WHMIS 2015
SUBCATEGORIES
SUBCATEGORIES

## Slide 24: Physical Hazard: Flame Pictogram
Self-Heating Substances and Mixtures (Category 1 & 2)
Substances and Mixtures which, in contact with water, emit flammable gases (Category 1, 2 & 3)
Self-Reactive Substances and Mixtures (Types B*, C, D, E & F)
Organic Peroxides (Types B*, C, D, E & F)
Flammable Liquids (Category 1, 2 & 3)
Flammable Aerosols (Category 1 & 2)
Flammable Solids (Category 1 & 2)
Flammable Gases (Category 1)
Pyrophoric Liquids (Category 1)
Pyrophoric Solids (Category 1)
Pyrophoric Gases (Category 1)
Products that will easily set on fire if ignited by a spark, static discharge or heat.
Examples: Gasoline, acetylene, acetone.
Classes that use this pictogram:

## Slide 25: Physical Hazard: Flame Over Circle Pictogram
Oxidizing liquids (Category 1)
Oxidizing solids (Category 1, 2 & 3)
Oxidizing gases (Category 1, 2 & 3)
Products that intensify fire, can cause combustible materials to ignite more readily, and may cause explosions.
Examples: Nitric acid, peroxides.
Classes that use this pictogram:

## Slide 26: Physical Hazard: Gas Cylinder Pictogram
Gases under pressure (compressed gas, liquefied gas, refrigerated liquefied gas, & dissolved gas)
Gases that are stored under pressure.
Examples: Oxygen, acetylene, propane.
Classes that use this pictogram:

## Slide 27: Physical Hazard: Corrosion Pictogram
Corrosive to Metals (Category 1)
Products that are corrosive to metals can damage or destroy metals.
Examples: Hydrochloric acid, sodium hydroxide.
Classes that use this pictogram:

## Slide 28: Physical Hazard: Exploding Bomb Pictogram
Self-Reactive Substances and Mixtures (Types A & B*)
Organic Peroxides (Types A & B*)
*Both the flame and explosive pictogram are used for type B Self-Reactive substances and mixtures, and type B organic peroxides.
Products are unstable and potentially reactive and/or explosive.
Examples: Nitroglycerin, picric acid.
Classes that use this pictogram:

## Slide 29: Physical Hazard Group Class: PHNOC
  Physical hazard presented by a product, mixture, material or substance that does not fit into any other physical hazard class.
  It characteristically occurs by chemical reaction and results in the serious injury or death of a person at the time the reaction occurs.
The label requires a pictogram that is applicable to the hazard, a hazard statement that describes the nature of the hazard, and the signal word "Danger".
Physical Hazards Not Otherwise Classified (PHNOC)

## Slide 30: Physical Hazard Classes Without Pictograms
  The following physical hazard classes and categories do not have a pictogram assigned to them. The label and SDS still require a signal word and hazard statement(s):
  Combustible dusts (Category 1)
          Any dust, that upon ignition, is able to catch fire or explode when dispersed in air.
  Simple asphyxiants (Category 1)
          Any gas that displaces oxygen in the air, and causes rapid suffocation.
  Flammable gases (Category 2)
  Flammable liquids (Category 4)
  Self-reactive substances & mixtures (Type G)
  Organic peroxides (Type G)

## Slide 31: Health Hazard Group
PHYSICAL
HAZARD GROUP
HEALTH HAZARD GROUP
PHYSICAL HAZARD GROUP CLASSES
HEALTH HAZARD GROUP CLASSES
CATEGORIES
CATEGORIES
WHMIS 2015
SUBCATEGORIES
SUBCATEGORIES

## Slide 32: Health Hazard: Health Hazard Pictogram
Respiratory sensitization (Category 1, 1A & 1B)
Germ cell mutagenicity (Category 1, 1A, 1B, & 2)
Carcinogenicity (Category 1, 1A, 1B, & 2)
Reproductive toxicity (Category 1, 1A, 1B, & 2)
Specific target organ toxicity following single exposure (Category 1 & 2)
Specific target organ toxicity following repeated exposure (Category 1 & 2)
Aspiration hazard (Category 1)
Products that cause or may cause serious health effects.
Examples: Benzene, lead (II) chromate.
Classes that use this pictogram:

## Slide 33: Health Hazard: Exclamation Mark Pictogram
Acute toxicity (oral, dermal, inhalation) (Category 4)
Skin corrosion/ irritation – Skin irritation (Category 2)
Serious eye damage/irritation - Eye irritation (Category 2 & 2A)
Respiratory or Skin sensitization – Skin sensitizer (Category 1, 1A & 1B)
Specific target organ toxicity -single exposure, (Category 3)
Not used with the "skull and crossbones" pictogram for skin or eye irritation if:
The "corrosion" pictogram also appears.
The "health hazard" pictogram is used to indicate respiratory sensitization.
Products that cause or may cause less serious health effects.
Examples: Xylene, benzene, acetone.
Classes that use this pictogram:

## Slide 34: Health Hazard: Skull & Crossbones Pictogram
Acute toxicity (oral, dermal, inhalation) (Categories 1, 2 & 3)
Products that can cause death or toxicity with short exposure to small amounts.
Examples: Carbon monoxide, cyanide, formaldehyde.
Classes that use this pictogram:

## Slide 35: Health Hazard: Corrosion Pictogram
Skin corrosion/irritation – Skin corrosion (Category 1, 1A, 1B & 1C)
Serious eye damage/irritation – Serious Eye Damage (Category 1)
Products that are corrosive to skin and eyes.
Examples: Sulfuric acid, hydrochloric acid, sodium hydroxide.
Classes that use this pictogram:

## Slide 36: Health Hazard: Bio-hazardous Infectious Materials Pictogram
Bio-hazardous infectious material (Category 1)
Organisms that have been shown to cause disease or are believed to cause disease in either humans or animals.
Examples: HIV and/or Hepatitis infected blood or saliva.
Classes that use this pictogram:

## Slide 37: Health Hazard Group Class: HHNOC
  Health hazard presented by a mixture or substance that does not fit into any other health hazard class.
  It characteristically occurs via acute or repeated exposure, and has an adverse effect on the health of a person exposed to it, including injury , or resulting in the death of that person.
The label requires a pictogram that is applicable to the hazard, a hazard statement that describes the nature of the hazard, and the signal word "Danger".
Health Hazards Not Otherwise Classified (HHNOC):

## Slide 38: Health Hazard Classes without Pictograms
  The following health hazard classes and categories do not have a pictogram assigned to them. The label and SDS still require a signal word and hazard statement(s):
  Serious eye damage/irritation – Eye Irritation (Category 2B)
  Reproductive toxicity – Effects on or via lactation

## Slide 39: Safety Data Sheets (SDS)
In WHMIS 2015, Material Safety Data Sheets (MSDS) are now referred to as Safety Data Sheets (SDS).
SDS for products must be supplied, by the supplier, to the buyer.
These sheets contain more detailed information about the product. This information is used to protect workers from hazards, to ensure proper use, handling and storage of the product, as well as emergency procedures.
During the WHMIS 1988/2015 transition period, either an MSDS or an SDS will be provided by the supplier.

## Slide 40: Safety Data Sheets (SDS)
SDS must have 16 sections and be in English and French.
SDS must be updated within 90 days of any new changes.
  SDS will identify:
          The product and the Canadian supplier.
    Any hazards associated with using the product.
    Precautions that need to be taken when using the product.
    Steps to take in the event of an emergency.
* You must have the SDS readily available when working with any hazardous products.

## Slide 41: SDS Sections
Physical and Chemical Properties
Stability and Reactivity
Toxicological Information
Ecological Information
Disposal Considerations
Transport Information
Regulatory Information
Other Information
Identification
Hazard Identification
Composition/Ingredients
First Aid Measures
Firefighting Measures
Accidental Release Measures
Handling and Storage
Exposure Controls/ Personal Protection
The following sections must be present on the SDS:
Under WHMIS 2015, providing information in sections 12, 13, 14 & 15 is optional; however, the headings are still required on the SDS.

## Slide 42: SDS Sections
Section 1: Identification
  Identifies the chemical on the SDS as well as the recommended uses.
  Provides essential supplier contact information.
Section 2: Hazard Identification
  Identifies the hazard(s) of the chemical and the appropriate warning information associated with those hazards.

## Slide 43: SDS Sections
Section 3: Composition/Ingredients
  Identifies the ingredient(s) contained in the product indicated on the SDS, including impurities and stabilizing additives.
  Includes information on substances, mixtures and all chemicals where a trade secret is claimed.
Section 4: First Aid Measures
  Describes the initial care that should be given to an individual who has been exposed to the chemical.

## Slide 44: SDS Sections
Section 5: Firefighting Measures
  Provides recommendations for fighting a fire caused by the chemical.
Section 6: Accidental Release
  Provides recommendations on the appropriate response to spills, leaks or releases, including containment and clean-up practices to prevent or minimize exposure to people, property, or the environment.
  May also include recommendations distinguishing between responses to large and small spills where the spill volume has a significant impact on the hazard.

## Slide 45: SDS Sections
Section 7: Handling and Storage
  Provides guidance on the safe handling practices and conditions for safe storage of chemicals.
Section 8: Exposure Controls/Personal Protective Equipment (PPE)
  Indicates the exposure limits, engineering controls, and PPE measures that can be used to minimize worker exposure.

## Slide 46: SDS Sections
Section 9: Physical and Chemical Properties
  Identifies physical and chemical properties associated with the substance or mixture.
Section 10: Stability and Reactivity
  Describes the reactivity hazards of the chemical and the chemical stability information.
  This section is broken down into three parts: reactivity, chemical stability, and other.
Section 11: Toxicological Information
  Identifies toxicological and health effects of exposure to the chemical, including lethal doses and symptoms of exposure.

## Slide 47: SDS Sections
Section 12: Ecological Information*
  Provides information to evaluate the environmental impact of the chemical if it were released to the environment.
Section 13: Disposal Considerations*
  Provides guidance on proper disposal practices.
Section 14: Transport Information*
  Provides guidance on classification information for shipping and transporting the chemical.
Section 15: Regulatory Information*
  Identifies the safety, health and environmental regulations that apply to the product.
Section 16: Other Information
  Indicates when the SDS was prepared or when a revision was made.
  * Information is not required to be provided for these sections. However, the headings must still appear on the SDS.

## Slide 48: Where To Find SDSs
All SDSs can be found at www.msdsforschools.ca.
If you need instructions on how to use the site, search the Board’s intranet site “MSDS instructions” to access the document.
Always have a hard copy of the SDS readily available when working with a product.

## Slide 49: Quiz
You’re now ready to complete the quiz.
You must receive 100% to pass the quiz.
You will have multiple attempts to receive 100% on the quiz.
Once you have completed and passed the quiz, don’t forget to hit the confirm button.

## Slide 50: Every hazardous product that falls under WHMIS must have:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
A label and an SDS.
B)
A packing slip and invoice.
C)
A label.
D)
A specific type of container.

## Slide 51: SDSs must be _______ , when working with any hazardous product:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Readily available, in paper or electronic form.
B)
In colour.
C)
In the supervisor's office.
D)
I don't need an SDS.

## Slide 52: Reading the SDS before you work with a product is important because:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
It provides more information than the label.
B)
It is required by the employer.
C)
The label provides the product name and pictogram.
D)
The SDS provides medical advice.

## Slide 53: Pictograms can easily be identified because they have a ___________ border, except for the Bio-hazardous & Infectious Material symbol which has a round black border. Fill in the blank.
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Red square on point (diamond)
B)
Black square on point
C)
All pictograms have a round black
D)
Pictograms do not have a border

## Slide 54: Who is responsible for ensuring that workers understand the hazards of the products that they work with?
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
The employer
B)
The union
C)
The Health and Safety department
D)
The Joint Health and Safety Committee

## Slide 55: When reading a product label, what can be used to figure out the nature and severity of the hazard?
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Read the hazard statements
B)
Understand the pictogram
C)
Check what signal word is present (Danger or Warning)
D)
All the above

## Slide 56: The signal word:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Describes the nature of the hazard.
B)
Describes measures to prevent or minimize the adverse effects.
C)
Alerts to the severity of the hazard.
D)
Gives supplier information.

## Slide 57: The hazard statement:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Describes the nature of the hazard.
B)
Describes measures to prevent or minimize the adverse effects.
C)
Alerts to the severity of the hazard.
D)
Gives supplier information.

## Slide 58: The precautionary statement:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Describes the nature of the hazard.
B)
Describes measures to prevent or minimize the adverse effects.
C)
Alerts to the severity of the hazard.
D)
Gives supplier information.

## Slide 59: This pictogram is used for which of the following classes:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Acute toxicity
B)
Carcinogenicity
C)
Serious eye damage
D)
Skin sensitization

## Slide 60: This pictogram is used for which of the following classes:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Acute toxicity
B)
Carcinogenicity
C)
Serious eye damage
D)
Skin sensitization

## Slide 61: A workplace label is not necessary when:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
A chemical is poured into a container for immediate use.
B)
The person who poured the product into another container will be the only person using it, and the chemical will be used during one shift.
C)
Workplace labels are never necessary
D)
A & B

## Slide 62: When a product is poured into a container, and a workplace label is not required, the container must still be identified/labelled with the product name.
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
True
B)
False

## Slide 63: This pictogram is used for which of the following classes:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Oxidizing solids
B)
Corrosive to metals
C)
Flammable liquids
D)
Gases under pressure

## Slide 64: The 3 legislated components of WHMIS are: labels, safety data sheets and training.
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
True
B)
False

## Slide 65: Under WHMIS 2015, the following types of products continue to be excluded from labelling and SDS requirements:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Consumer Products
B)
Explosives
C)
Pesticides
D)
All the above

## Slide 66: WHMIS 2015 supplier labels will have:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Hatched border, symbol in a black circle, no standardized phrases.
B)
Hatched border, symbol in a red square on its point, no standardized phrases.
C)
Solid border, symbol in a red square on its point, standardized phrases.
D)
None of the above

## Slide 67: A workplace label is required when a chemical is poured into a new container. The label must include:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Product identifier or Name
B)
Safety handling precautions
C)
Reference to the Safety Data Sheet
D)
All the above

## Slide 68: This pictogram is used on products that:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Will easily set on fire if ignited by a spark, static discharge or heat.
B)
Are corrosive to metals and skin
C)
Contain flammable liquids, solids and gases
D)
A and C

## Slide 69: This pictogram is used on products that are oxidizers. These products intensify fire, can cause combustible materials to ignite more readily, and may cause explosions.
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
True
B)
False

## Slide 70: This pictogram is used on products that:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Intensify fire, can cause combustible materials to ignite more readily, and may cause explosions.
B)
Will easily set on fire if ignited by a spark, static discharge or heat.
C)
Will damage or corrode metal, skin and eyes.
D)
Will clean hands and metal.

## Slide 71: This pictogram is used on products that are unstable and potentially reactive and/or explosive.
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
True
B)
False

## Slide 72: This pictogram is used on products that cause, or may cause, serious health effects.
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
True
B)
False

## Slide 73: Safety Data Sheets:
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
Have 16 sections
B)
Must be in English and French
C)
Must be updated within 90 days of any changes
D)
All the above

## Slide 74: The lower (smaller) the category number assigned to a hazard class the less hazardous the chemical is.
Correct - Click anywhere to continue.
Incorrect - Click anywhere to continue.
You answered this correctly!
Your answer:
The correct answer is:
You did not answer this question completely
You must answer the question before continuing.
Submit
Clear
Try again.
A)
True
B)
False

## Slide 75: Quiz
Your Score | {score}
Max Score | {max-score}
Number of Quiz Attempts | {total-attempts}
Question Feedback/Revie
w Information Will Appear Here
Review Quiz
Continue

## Slide 76
Now that you have completed this training module, click the confirm button below to submit the certificate of completion to our database.
IMPORTANT!
CONFIRM